## Slide 1: Weaponized WiFi Attack Tool
Hacking WPA for fun and profit
Jiaheng Wang @Alibaba Inc.
Jun Xie @Alibaba Inc.

## Slide 2: About us
Jiaheng Wang Security Researcher @IoT security Research Team
Jun Xie Head of IoT Security Research Team in Alibaba
Focus on Internet Of Things Security Research, Reverse engineering, hardware hacking, Drones, Smart devices
Twitter:@vessial

## Slide 3: Outline
Background
Man-One-The-Side(MOTS) Attack in WPA2 encrypted network
Side-Relay Attack On WPA Network
Attack Tools
Future work

## Slide 4: Background
Brief of the well-known WPA/WPA2 standard

## Slide 5: Background
WPA Encryption - Frame Control
Data is encrypted or not
Sequence Number

## Slide 6: Background
WPA Encryption - QoS Data Packet
Type = 0x02
Subtype = 0x08

## Slide 7: Background
WPA Encryption - QoS Data Packet Body
Packet Number(IV)

## Slide 8: Attack in Encrypted Network
What is a good WLAN attack?
  Hidden – No fake AP or connection needed.
  Flexible – Support both 2.4G & 5G bands
  Precision – Precisely attack to each single user.
  Portable – Tool in tiny Size

## Slide 9: Prerequisites for an attack
The ESSID(name) of the target AP
The BSSID (Mac address) of AP
The pre-shared password(or leak for PTK) of the network.(Just for key calculation)
The MAC address of the victim.

## Slide 10: Attack in Action – Stage 1
Man-On-The-Side(MOTS) Attack in a WPA/WPA2 Encrypted Network
  Example: DNS Spoof in Encrypted Network.

## Slide 11: Attack in Action – Stage 1
DNS Spoof in Encrypted Network
Normal state

## Slide 12: Attack in Action – Stage 1
DNS Spoof in Encrypted Network
Under Attack

## Slide 13: Attack in Action – Stage 1
Important
  Match sequence number
  Correct Packet Number
  Reconstruct QoS Data Packet

## Slide 14: Attack in Action – Stage 1
DNS Spoof in Encrypted Network
  Active De-authenticate the device and capture handshakes or Passive Capture new handshakes.
  Calculate STA new PTK via the 4-way handshake
  Reconstruct DNS response and inject back to network.

## Slide 15: Attack in Action – Stage 1
DNS Spoof in Encrypted Network

## Slide 16: Attack in Action – Stage 1
DNS Spoof in Encrypted Network
  Important! Match sequence number

## Slide 17: Attack in Action – Stage 2
Attack in a WPA/WPA2 Encrypted Network
  Stage 2:
    DoS Attack

## Slide 18: Attack in Action – Stage 2
DoS Attack
  Set Packet Number to a large value
Normal State
Large PN Attack

## Slide 19: Attack in Action – Stage 3
Side Relay Attack in a WPA/WPA2 Encrypted Network
  Similar to MITM Attack
  Attacker can modify 802.11 packet data retransfer to the victim.

## Slide 20: Attack in Action – Stage 3
Side Relay Attack in a WPA/WPA2 Encrypted Network
  Repack QoS data packet from AP

## Slide 21: Attack in Action – Stage 3
Side Relay Attack Detail

## Slide 22: Demos
Because of the attack effect depends on the wireless environment.
Live demo may not show good effect and need about 10min to setup.
To save time, we will show a video first.
If you are interested in a live demo.
Suggested to contact us after the talk.

## Slide 23: DEMO Stage 1 MOTS Attack
Inject Fake DNS Packet to spoof the victim.

## Slide 24: Demo Setup

## Slide 25: DEMO Stage 2 PN DoS Attack
Inject Large Packet Number cause DoS to one victim.

## Slide 26: Demo Setup

## Slide 27: DEMO Stage 3 Side Relay Attack
Inject Large Packet Number cause DoS to one victim.
And then Relay Packet from AP with a modified PN to victim
(Data also can be modified)

## Slide 28: Demo Setup
Assuming DoS Stage has succeeded.

## Slide 29: Attack Tool
80211Killer
Features:
BCM43340 Based
Support 2.4G and 5G band
OS: ThreadX 5.6
Tiny size
Any packet injection
Monitor mode
Portable

## Slide 30: Attack Tool
Get Full control of BCM43340 80211MAC layer
  Enable packet Injection (Thanks to nexmon[*] project.)
  Get control of sequence number (patch d11 core microcode)
[*]See Here https://github.com/seemoo-lab/nexmon

## Slide 31: Attack Tool
Broadcom WLAN SoC

## Slide 32: Attack Tool
b43 assemble
D11 Micro Code
*Original photo is stolen from Project Zero.
See here: http://goo.gl/zxzEK6

## Slide 33: Attack Tool
b43 assemble
  Undocumented
  Ugly
  Long and complicated

## Slide 34: Attack Tool
b43 assemble
  R9 - Probably Sequence Counter
  Special Purpose Register 0EE
    Sequence Control Field in TME
Notice: The register layout may
be different between chips

## Slide 35: Attack Tool
Transmit Modify Engine(Simplified Graph)
Firmware
TXE
TME
microcode
PHY
Modify Duration/ID & Sequence Control

## Slide 36: Attack Tool
But How to find the address of SPR0EE?
  Differential Analysis

## Slide 37: Attack Tool
Sequence Control Register
  Address offset is 0x5dc
  D11 Core Base is 0x18001000
  Notice: 0x5dc is for bcm43340 soc, but for bcm4356 is 0x5e2

## Slide 38: Attack Tool
Let’s Patch it!
Just comment it!! :P

## Slide 39: Attack Tool
Finally set sequence number in Firmware

## Slide 40: Attack Tool
Similar work also done on NanoPC T4
  NanoPC T4 uses AP6356S(BCM4356) and support 2x2 MIMO
  Provide higher performance

## Slide 41: About capture capability
All attacks we introduced today is highly based on packet capture.
  More powerful wireless card for capture will perform better in attack.
  For 3x3 MIMO wireless card of victim, we need wireless card support 3x3 MIMO to capture the data packets.
  For MU-MIMO wireless network, we should stay in the same petal with the victim.

## Slide 42: Compare
 | MOTS | Side Relay Attack
Open Network | affected | Unaffected????
WPA/WPA2-Personal | affected | affected
WPA3-Personal[1] | Part affected* | Part affected*
WPA/WPA2/WPA3-Enterprise | Part affected* | Part affected*
[1]Notice: Wi-Fi Alliance announced that WPA3 uses Dragonfly Key Exchange Protocol, which provides forward secrecy. So we can’t reconstruct the TK just through the handshake packet and the pre-shared key.
*Though we can’t just reconstruct the TK from knowing password, it does not mean that the three attack can’t be performed.
If the TK is leaked in other way, the three attack also can be perfomed. So we mark as part affected.
It is also very interesting that the open network is not affected by Side Relay Attack.

## Slide 43: What’s special of this attack?
In God View we believe(on 802.11 MAC layer)
Vulnerability or not vulnerability this is a question
Wi-Fi Jack
DNS hijack
IP hijack
ARP spoof
TCP hijack

## Slide 44: Mitigation
Use WPA3
Deploy WPA/WPA2-Enterprise
Deploy 802.11w management frame protection.
Application use C2C/S trust compute model(e.g., trusted certificate auth)

## Slide 45: Future work
Firmware Symbiotes on Wi-Fi chips
Building hardware fuzzing platform for Wi-Fi chips
Find baseband vulnerability to exploit Wi-Fi chip without PSK (e.g. BroadPwn)

## Slide 46: Questions? Thank you